## Slide 1: Digital twin for wind energy industry
Adrien Hirvoas, Ph.D. - FEM
ISEN Yncréa Ouest

## Slide 2: Digital twin for wind energy industry
Day 1: Welcome and Introduction Why wind energy ? Digital Twin Overview Practical work - Python: TP – Python introduction TP – Pandas introduction TP – Anomaly detection introduction | Day 2: Introduction Overview of OpenFAST Practical work: Inputs and outputs workflow Running OpenFAST OpenFAST Modules OpenFAST tool: python-toolbox Practical work: Practicing Run your first simulation | Day 3: OpenFAST reminder OpenFAST tutorial Practical work: Post-Processing A digital twin approach Anomaly detection Conclusion & Question

## Slide 3: Day 2 - Agenda
Introduction
Overview of OpenFAST
OpenFAST modules
Practice – Offshore wind turbine

## Slide 4: Introduction – Numerical modelling
Why?
Lower wind cost of energy requires technology advancement through improved engineering capability founded on physics.
What?
Improved physics-based engineering design competence and software needed to advance wind energy technology.
How?
Use the knowledge, data, and results from broader wind research to improve physics-based engineering design competence and software.
Engineering Design Competence and Models
Physic-Based
Knowledge
Real-World
Data
Advanced Wind
Energy
Technology at
Lower Cost

## Slide 5: Introduction – Numerical Modelling
Coupling Between Fluids, Structures, and Controls
Aerodynamics
Structures
Controls
Hydrodynamics

## Slide 6: Introduction – Digital Twin Goal
Digital Twin - Wind Turbine
What for ?
Improve availability
Reduce operational expenditure (OPEX)
Streamline inspection
Anticipate life extension
Improve future designs

## Slide 7: Introduction – Digital Twin Benefits
 | Full sensor monitoring | Numerical monitoring | DT monitoring
Installation & maintenance costs |  |  | 
Accuracy |  |  | 
Reliability |  |  | 

## Slide 8: Day 2 - Agenda
Introduction
Overview of OpenFAST
OpenFAST modules
Practice – Onshore wind turbine

## Slide 9: Overview of OpenFAST
OpenFAST: An Open-Source Tool for Wind Turbine Physics-Based Engineering Modeling
An open-source wind turbine physics-based engineering tool
Mathematical models are implemented in distinct modules & interconnected to solve for the global, coupled, dynamic response of a system
Currently an open-source code-development community for physics-based engineering models

## Slide 10: Overview of OpenFAST
OpenFAST - inputs and outputs
Main.out
Main*.sum
Main*.ech
…
vtk*/
Main*.lin
INPUTS:
one main file (extension .fst) which references other files
OUTPUTS:
one data file (.out or .outb) with time series of selected output channels
optional files: summary (.sum), echo (.ech), linearization (.lin), visualization (vtk)
Main.fst
ElastoDyn.dat
AeroDyn.dat
ED_Tower.dat
ED_Blade.dat
….
AD_Blade.dat
Polar.dat
Time (s) | Rotor Speed (rpm) | … | Channel[n] (unit)
0 | 5.0 |  | 
0.1 | 4.9 |  | 
… | … |  | 
tMax | 5.5 |  | 
OpenFAST executable

## Slide 11: Overview of OpenFAST
INPUTS
OUTPUT
Typical folder:
EXE
OpenFAST - inputs and outputs (in practice)

## Slide 12: Day 2 - Agenda
Introduction
Overview of OpenFAST
OpenFAST modules
Practice – Offshore wind turbine

## Slide 13: OpenFAST modules
Primary (.dat)
ElastoDyn | Structural dynamics
Primary (.dat)
AeroDyn | Aerodynamics
Primary (.dat)
InflowWind |
Wind Inflow
Primary (.dat)
ServoDyn |Control and Electrical Drive Dynamics
Primary (.dat)
HydroDyn |Hydrodynamics
Primary (.dat)
MAP++ |Quasi static Mooring Dynamics
OpenFAST driver
Primary (.fst)
Additional ElastoDyn input files (.dat)
Additional AeroDyn input files (.dat)
Wind data files (.wnd, .bts, hh, etc…)
Bladed-style external controller (.dll)
Additional HydroDyn input files (.dat)
Times Series (.out, .outb)
Linearization (.lin)
Visualization (.vtp)

## Slide 14: OpenFAST modules
ElastoDyn
  Computes structural response as part of the aero-hydro-servo-elastic solution
    Combined modal & multi-body representation through 24 Degrees of Freedom
      Multi-body: platform, nacelle, generator, gears, hub, tail
      Modal: blades, tower
    Blade & tower modeling assumptions:
      Bernoulli-Euler beams
      Straight & isotropic
      Bending only
      Small to moderate deflections
Modal
representation

## Slide 15: OpenFAST modules
AeroDyn
  Computes aerodynamics (lift, drag, pitch) as part of the aero-elastic solution
    Wind-inflow input:
      Uniform, unsteady
      Turbulent (TurbSim)
    Wake modeling:
      Blade Element Momentum (BEM) theory
      Dynamic wake (DBEMT)
      Dynamic stall modeling:
      Beddoes-Leishman (semi-empirical)
      Tower drag & influence on wind
Schematic representing an annular actuator in BEM theory from [8]

## Slide 16: OpenFAST modules
InflowWind
  Undisturbed wind inflow:
    Steady
    Uniform, but time-varying, e.g., deterministic gusts from IEC (IECWind)
    Full-field (FF) turbulence (TurbSim, Mann)
    User-defined

## Slide 17: OpenFAST modules
ServoDyn
  Control and Electrical Drive Dynamics
    Modeling: standard conventional pitch controller
      Two main operating regimes:
        Maximum Power Regime
        Constant Power Regime
  Floating context: problems due to negative damping

## Slide 18: OpenFAST modules
HydroDyn
  Computes wave-kinematics & hydrodynamics as part of the hydro-elastic solution
    Waves & Current
      Wave kinematics:
        Linear regular (periodic)
        Linear irregular (stochastic):
      Wave direction & directional spreading
    Steady sea currents:
      IEC-style sub-surface, near surface, & depth-independent
      Or user-defined
    Hydrodynamic Loading
      Strip theory (Morison)
      Potential flow (WAMIT):
        1st and 2nd-order (QTF or Newman’s approximation) theory
      Hybrid combination of these two
Multi-Directional Sea State
IEC Sea Currents

## Slide 19: OpenFAST modules
MAP++
  Quasi static
  Multi-segmented array of taut or catenary lines
  Elastic stretching
  Apparent weight of lines
  Clump weights & buoyancy tanks
  Seabed friction
  Nonlinear geometric
Constraint States:
Displacements
Velocities
Parameters:
Line properties
Line connectivity
Gravity
Inputs:
Platform displacements
Outputs:
Line tensions
Line displacements
MAP++ module

## Slide 20: Day 2 - Agenda
Introduction
Overview of OpenFAST
OpenFAST modules
Practice – Offshore wind turbine

## Slide 21: Practice – Offshore wind turbine – Google Colab
What is Google Colab?
  Google Colab which stands for Google Colaboratory is a cloud platform
  provided by Google to run Python Notebook’s without need to install
  anything on your local machine.
Features of Google Colab
  Zero Setup Required
  Free GPU Access
  Pre-installed Libraries
Accessing Google Colab
  https://github.com/Ahirvoas/Training-Day2/blob/main/Tutorial_day2.ipynb